## Slide 1: Azure Percept Home Automation
Sat, May 28 | 1PM ET | 5PM PT
Livestream event
Peter Gallagher
IoT Consultant – PJG Creations Ltd

## Slide 2: Azure Percept Home Automation
Pete Gallagher
Petecodes.co.uk / pjgcreations.co.uk

## Slide 3: About Me
Pete Gallagher @pete_codes
www.PeteCodes.co.uk
peter.gallagher@octopus.com
Senior Solutions Architect at Octopus Deploy
Microsoft Certified Trainer & Azure MVP, Pluralsight Author
Decades of Desktop, Web & Embedded Software experience,
Meetup Organiser,
STEM Ambassador, Code Club Organiser … Gadget Addict
Father of two inquisitive girls

## Slide 4
Azure Percept

## Slide 5
Azure Percept Hardware
Vision Module
Carrier Board
Audio Module

## Slide 6
Azure Percept – Carrier Board
NXP iMX8m processor
Trusted Platform Module (TPM) version 2.0
Wi-Fi and Bluetooth connectivity
1x Ethernet 2x USB-A 3.0 1x USB-C
Microsoft CBL-Mariner Linux Distro
Microsoft Azure IoT Edge
Percept Studio

## Slide 7
Azure Percept – Vision Module
Intel Movidius Myriad X (MA2085) Vision Processing Unit (VPU) with Intel Camera ISP integrated @ 0.7 TOPS
Sony IMX219 Camera sensor with 6P Lens
8MP at 30FPS
50cm to infinity focussing
120 degree Field of View
Custom Vision
No Code AI Solution

## Slide 8
Azure Percept – Audio Module
XMOS XUF208 Codec
4x MEM Sensing Microsystems Microphones Linear Array
3.5 mm Audio Out
Speech Services and Azure Speech Studio
No Code AI Solution

## Slide 9
Azure Percept Components
IoT Hub and Edge
Speech Services and Speech Studio
Custom Vision

## Slide 10
Percept Vision and Audio Demos

## Slide 11
Percept Home Automation

## Slide 12
Percept Home Automation
Azure Percept Audio
Speech
Azure Function
IoT Hub
Raspberry Pi
Mains Relay
Desk Lamp

## Slide 13
Percept Home Automation Demo

## Slide 14
Links
  Blog Post https://bit.ly/percept-home-automation
  GitHub Repo https://bit.ly/percept-home-automation-repo
  Azure Percept http://bit.ly/azure-percept
  Azure Speech Services http://bit.ly/azure-speech-services
  Azure Custom Vision http://bit.ly/azure-custom-vision
  Cloud Skills Challenge https://aka.ms/StudentDeveloperDayChallenge

## Slide 15: IoTeaLive
https://twitch.tv/azureishlive

## Slide 16
pluralsight.pxf.io/az220

## Slide 18: Thursday 12th May from 18:30 BST ON ZOOM!
Laurent Ellerbach Principle Software Engineer - Microsoft
.NET nanoFramework

## Slide 20
Twitter @pete_codes
Email: peter.gallagher@octopus.com
Personal Website: https://www.petecodes.co.uk Notts IoT: https://www.nottsiot.co.uk
Dot Net Notts: https://www.dotnetnotts.co
Notts Dev Workshop: https://www.nottsdevworkshop.co.uk
LATi: https://www.lati.org.uk
Agile Engineering Podcast: https://agileengineeringpodcast.com/
Azureish Live: https://www.twitch.tv/azureishlive
Contact Me
Slides: https://bit.ly/pjgai422022